## Slide 1: Diffusion Model Acceleration on FPGA
Hongwu Peng1, Amit Hasan1, Xi Xie1, Jiahui Zhao1
1University of Connecticut, Connecticut, USA

## Slide 2: Outline
Background
Algorithm Design
  Stable Diffusion Algorithm
  Model Structure
  Inference Iterations
Hardware Design
  System Setup
  Coarse Grained Pipelining Architecture
  Fully Connected Layer Hardware Design
  Convolutional Layer Hardware Design
  Latency Evaluation
Conclusions

## Slide 3: Background
Stable Diffusion is a deep learning, text-to-image model released in 2022. It is primarily used to generate detailed images conditioned on text descriptions, though it can also be applied to other tasks such as inpainting, outpainting, and generating image-to-image translations guided by a text prompt.
An image generated by Stable Diffusion based on the text prompt "a photograph of an astronaut riding a horse"

## Slide 4: Background
Stable Diffusion uses a variant of diffusion model (DM), called latent diffusion model (LDM).
The typical stable diffusion model consists of 3 parts: the variational autoencoder (VAE), U-Net, and an optional text encoder. The VAE encoder compresses the image from pixel space to a smaller dimensional latent space, capturing a more fundamental semantic meaning of the image. Gaussian noise is iteratively applied to the compressed latent representation during forward diffusion. The U-Net block, composed of a ResNet backbone, denoises the output from forward diffusion backwards to obtain latent representation. Finally, the VAE decoder generates the final image by converting the representation back into pixel space.

## Slide 5: Stable Diffusion Algorithm
encoder
latent space
astronaut
+
noise
denoise
latent space
astronaut
decoder
encoder
latent space
riding a horse
+
noise
denoise
latent space
riding a horse
decoder
+
+
After training:
denoise
latent space
astronaut riding a horse
decoder
+

## Slide 6: Conditional Stable Diffusion
Encoder
Decoder
Image size: 28 x 28
Image size: 28 x 28
Image with noise
Predicted noise
Reconstructed image
Subtract noise from input image with noise
Condition
The digit to be generated
Loop through the steps
Latent space

## Slide 7: Training the Model
U-Net down
U-Net up
Image size: 28 x 28
Image size: 28 x 28
Image with noise
Predicted noise
Reconstructed image
Subtract noise from input image with noise
8
The digit to be generated
Converted to embedding
Diffusion timestep
Training sample
generation
Timestep, t = 0
Timestep, t = 1
Timestep, t = 2
Timestep, t = k
Add noise
Add noise
Add noise
Skip connections
Latent space
Convolution layer
Maxpool layer
Deconvolution layer

## Slide 8: Inference Iterations
U-Net down
U-Net up
Image size: 28 x 28
Image size: 28 x 28
Image with noise
Predicted noise
Reconstructed image
Subtract noise from input image with noise
8
The digit to be generated
Converted to embedding
Diffusion timestep
Loop through Diffusion timestep = K, K-1, K-2, …., 3, 2, 1
Convolution layer
Maxpool layer
Deconvolution layer
Skip connections
Latent space

## Slide 9: System Setup
CPU
AXI4 Interconnect
Programable logic:
FPGA Overlay
Interrupt
DRAM
System overview:
CPU controls the start of FPGA. The FPGA overlay signal an interrupt back to the CPU, indicating the job has finished.
CPU and FPGA have a system-on-chip architecture, so they have shared main memory resources.
CPU will allocate the necessary memory for FPGA to support computation.

## Slide 10: Coarse Grained Pipelining Architecture
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Input Buf1
Input Buf0
Out Buf1
Out Buf0
DRAM
Data Loader
Data Writer
Architecture overview:
Data Loader: Load the weight, activation, and bias data from DRAM to the on-chip buffer.
Process Element Group: Consists of process elements that conduct the general computation, such as (X·W+b).
Data Writer: Write the output from the on-chip buffer back to DRAM.
Double Buffer to organize between data transfer & compute
Coarse-grained pipeline architecture
CPU
AXI4 Interconnect

## Slide 11: Coarse Grained Pipelining Architecture
Feature:
Use the double buffer to hide computation/communication latency and increase hardware utilization.
Carefully design the load and write sequence in an efficient way to reduce memory traffic.
if (pingpong)
{
load(in_buf0, DDR);
compute(in_buf1, out_buf1);
write(out_buf0, DDR);
pingpong = ~ pingpong;
{
load(in_buf0, DDR);
compute(in_buf1, out_buf1);
write(out_buf0, DDR);
pingpong = ~ pingpong;
}
Pseudo code for computation
Load0
Comp1
Write0
Load1
Comp0
Write1
Load0
Comp1
Write0
Time
Latency hiding with coarse-grained pipeline

## Slide 12: Fully Connected Layer Hardware Design
FC Layer computation:
Y = X·W + b
FC Layer hardware design:
Divided the vector-matrix multiplication into task blocks.
The memory load, compute, memory write scheduling between blocks follows the coarse-grained pipeline design
Task division
Fully connected layer operator
×
+
=
×
=
×
Conducted on device
……
X
W
b
Y
X1
W1
=
Y1
+
Y1
X1
W1
×
=
×
Conducted on device
X1
W2
=
Y2
+
Y2
X1
W2

## Slide 13: Convolutional Layer Hardware Design
Con2D Layer computation:
Input: X[Cin][Hin][Win] (input), W[Cin][Cout][K][K]
Output: Y[Cout][Hout][Wout] (out)
Conv2D hardware design:
Divided the Conv2D into sub-task blocks.
The memory load, compute, memory write scheduling between blocks follows the coarse-grained pipeline design
Task division

## Slide 14: Latency Evaluation
 | Alienware with RTX 3060 GPU | PYNQ-Z2
Platform Power | 150 W | 5 W
Time to generate singe image | 14 s | 127 mins
Efficiency | 2.1 k(W·s)/image | 38.1 k(W·s)/image
FPGA is still lower than GPU for regular computation.
Main reason:
Pynz-Z2 is an old version of the FPGA board, and the process technology is not as good as RTX 3060
FPGA needs a more dedicated design to boost performance.
In terms of regular computation, FPGA is not as good as GPU. FPGA is more suitable for irregular computation, such as sparse matrix multiplication.

## Slide 15: Thank you!